## Slide 1
Flying and Judging F3A
F3A P-25 飞行与评分指南
SCHEMATIC MANOEUVRE ILLUSTRATIONS
SCHEDULE P-25

## Slide 3
图形注释 Explanations:
正飞 Aircraft upright
倒飞 Aircraft inverted
正面向内的侧飞
Aircraft in Knife-Edge View from Top
背面向内的侧飞
Aircraft in Knife-Edge View from Below
参考点 reference points
位滚 part roll
横滚 roll
快滚 snap rolls
正飞螺旋 pos. spin
neg.
半滚 half roll
¼
pos.
倒飞螺旋 neg. spin

## Slide 4
1200
安全线
Safety line
风向 wind
起飞程序
（不计分，不评分）
Take-off procedure
( not judged, not scored )

## Slide 5
P-25.01.01
倒飞进入，通过中心线拉1/8圆弧，进入45°向下直线，连续做两个1/4位滚，推3/8圆弧进入倒飞，在底边中间位置做一周横滚，推3/8圆弧进入45°向上直线，连续做两个1/4位滚，拉1/8圆弧，倒飞改出。From inverted, in the center pull through a one eighth loop into a forty-five degree downline, perform consecutively two quarter rolls, push through a three eighths loop, perform a roll, push through a three eighths loop into a forty-five degree upline, perform consecutively two quarter rolls, pull through a one eighth loop, exit inverted.
一周滚
¼ 位滚
¼ 位滚
¼ 位滚
¼ 位滚
P-25.01 三角筋斗带滚
Triangle from Top with two quarter rolls, roll, quarter rolls

## Slide 6
P-25.01.02
¼
¼
¼
¼
45°
所有圆角半径相等All radii are equal.
两个¼位滚在直线段的中间
¼ rolls centered on middle of the line.
两个¼位滚之间的线段必须短且长度易于辨识。
Lines between part rolls must be short and of recognisable length.
横滚位于直线段的中间
Roll in the center.
P-25.01 三角筋斗带滚
Triangle from Top with two quarter rolls, roll, quarter rolls

## Slide 7
P-25.02.01
倒飞进入，拉1/4圆弧进入垂直下降直线，做一周横滚，拉1/4圆弧，正飞改出。
From inverted, pull through a quarter loop into a vertical downline, perform a roll, pull through a quarter loop, exit upright.
一周横滚
P-25.02 半方筋斗带一周滚
Half Square Loop with roll

## Slide 8
P-25.02.02
横滚位于直线段的中间
Roll on middle of the line.
P-25.02 半方筋斗带一周滚
Half Square Loop with roll
所有圆角半径相等All radii are equal.

## Slide 9
P-25.03.01
正飞进入，通过中线拉1/8圆弧进入45°上升直线，做半滚，推1/4圆弧进入45°上升直线，做半滚，拉1/4圆弧进入45°下降直线，做半滚，推1/4圆弧进入45°下降直线，做半滚，拉1/8圆弧，正飞改出。
From upright, in the center pull through a one eighth loop into a forty-five degree upline, perform a half roll, push through a quarter loop into a forty-five degree upline, perform a half roll, pull through a quarter loop into a forty-five degree downline, perform a half roll, push through a quarter loop into a forty-five degree downline, perform a half roll, pull through a one eighth loop, exit upright.
半滚
半滚
半滚
半滚
P-25.03 斜方筋斗，四边带半滚
Square Loop on corner with half roll, half roll, half roll, half roll

## Slide 10
P-25.03.02
半滚位于直线段的中间
½ rolls on middle of the line.
45°
P-25.03 斜方筋斗，四边带半滚
Square Loop on corner with half roll, half roll, half roll, half roll
所有圆角半径相等All radii are equal.

## Slide 11
P-25.04.01
正飞进入，拉1/4圆弧进入垂直上升直线，做半滚，拉3/4圆弧，正飞改出。
From upright, pull through a quarter loop into a vertical upline, perform a half roll, pull through a three quarter loop, exit upright.
半滚
P25.04 9字带半滚
Figure Nine with half roll

## Slide 12
P-25.04.02
所有圆角半径相等All radii are equal.
半滚位于直线段的中间
½ rolls on middle of the line.
P25.04 9字带半滚
Figure Nine with half roll

## Slide 13
P-25.05.01
正飞进入，连续做三个1/4位滚，紧接着再做反向连续三个1/4位滚，正飞改出。
From upright, perform consecutively three quarter rolls, followed by three consecutive quarter rolls in opposite direction, exit upright.
¼ 位滚
¼ 位滚
¼ 位滚
¼ 位滚
¼ 位滚
¼ 位滚
P-25.05 六位双向1/4滚
Roll Combination with three quarter rolls, three quarter rolls in opposite direction

## Slide 14
P-25.05.02
¼
¼
¼
¼
¼
¼
在两个反向滚之间不能有直线段。
Between rolls and part rolls in opposite direction there must be no line.
¼位滚之间的线段必须短且长度易于辨识。
Lines between part rolls must be short and of recognisable length.
P-25.05 六位双向1/4滚
Roll Combination with three quarter rolls, three quarter rolls in opposite direction

## Slide 15
P-25.06.01
正飞进入，拉1/4圆弧进入垂直上升直线，做失速倒转进入垂直下降直线，做半滚，推1/4圆弧，倒飞改出。
From upright, pull through a quarter loop into a vertical upline, perform a stall turn into a vertical downline, perform a half roll, push through a quarter loop, exit inverted.
P-25.06 失速倒转带半滚
Stall Turn with half roll
半滚
围绕重心倒转Pivot on CG
倒转前有短暂停顿Stop before pivot (slight hesitation)

## Slide 16
P-25.06.02
围绕重心倒转Pivot on CG
倒转前有短暂停顿Stop before pivot (slight hesitation)
偏移幅度大于等于两倍翼展 = 0分
Two wing spans or more – zero points!
P-25.06 失速倒转带半滚
Stall Turn with half roll
半滚位于直线段的中间
½ rolls on middle of the line.
所有圆角半径相等All radii are equal.

## Slide 17
P-25.07.01
倒飞进入，做横滚一周后立即推起做半筋斗，紧接着做1/4位滚进入侧飞直线，做1/4位滚恢复正飞，紧接着推半筋斗接半滚，正飞改出。
From inverted, perform a roll, push through a half loop, perform a quarter roll into knife-edge flight, perform a quarter roll (back to upright flight), push through a half loop, perform a half roll, exit upright.
¼ 位滚
P-25.07 双殷麦曼带滚
Double Immelman with roll, quarter roll, quarter roll, half roll
半滚
¼ 位滚
一周滚
侧飞直线

## Slide 18
P-25.07.02
½ roll
¼
¼
第二段1/2圆弧必须紧接着1/4滚
The second half loop must follow immediately after the ¼ roll.
半筋斗必须紧跟在横滚之后
The half loop must follow immediately after the roll.
侧飞直线，机翼必须保持与地面垂直
During the knife edge the wing must be in the vertical plane.
第一个1/4滚必须紧接着半筋斗
The first ¼ roll must follow immediately after the half loop.
半滚必须紧接着半筋斗
The ½ roll must follow immediately after the second half loop.
P-25.07 双殷麦曼带滚
Double Immelman with roll, quarter roll, quarter roll, half roll
所有圆角半径相等All radii are equal.

## Slide 19
P-25.08.01
P-25.08 驼峰带双向半滚+半滚
Humpty Bump with two consecutive half rolls in opposite direction, half roll
正飞进入，拉1/4圆弧进入垂直上升直线，做双向半滚，推半筋斗进入垂直下降直线，做半滚，拉1/4圆弧，正飞改出。
From upright, pull through a quarter loop into a vertical upline, perform consecutively two half rolls in opposite direction, push through a half loop into a vertical downline, perform a half roll, pull through a quarter loop, exit upright.
半滚
半滚
半滚

## Slide 20
P-25.08.02
P-25.08 驼峰带双向半滚+半滚
Humpty Bump with two consecutive half rolls in opposite direction, half roll
所有圆角半径相等All radii are equal.
半滚位于直线段的中间
½ rolls on middle of the line.
在两个反向半滚之间不能有直线段。
Between rolls and part rolls in opposite direction there must be no line.

## Slide 21
P-25.09.01
正飞进入，做一个筋斗，在筋斗的第二段90°圆弧上做1/2同步滚，紧接着在第三段90°圆弧上反向做1/2同步滚，正飞改出。
From upright, pull through a loop while integrating a half roll in the second ninety degrees and another half roll in opposite direction in the third ninety, exit upright.
½ 同步滚
P-25.09 筋斗带双向1/2同步滚
Loop with two half rolls integrated
½ 同步滚

## Slide 22
P-25.09.02
½ 滚转同步
½ 滚转同步
90°
90°
筋斗必须是正圆
Loop must be round.
½滚必须与1/4圆弧的轨迹同步
½ rolls must be integrated on circular flightpath of the quarter loops.
P-25.09 筋斗带双向1/2同步滚
Loop with two half rolls integrated

## Slide 23
P-25.10 半斜方筋斗带半滚
Half Square Loop on Corner with half roll, half roll
P-25.10.01
正飞进入，拉1/8圆弧进入45°上升直线，做半滚，推1/4圆弧进入45°上升直线，做半滚，拉1/8圆弧，倒飞改出。
From upright, pull through a one eighth loop into a forty-five degree upline, perform a half roll, push through a quarter loop into a forty-five degree upline, perform a half roll, pull through a one eighth loop, exit inverted.
半滚
半滚

## Slide 24
P-25.10.02
45°
P-25.10 半斜方筋斗带半滚
Half Square Loop on Corner with half roll, half roll
所有圆角半径相等All radii are equal.
半滚位于直线段的中间
½ rolls on middle of the line.

## Slide 25
P-25.11.01
倒飞进入，拉1/4圆弧进入垂直下降直线，做半滚，推3/4圆弧进入水平直线，做半滚进入倒飞，拉3/4圆弧进入垂直上升直线，做半滚，推1/4圆弧，正飞改出。
From inverted, pull through a quarter loop into a vertical downline, perform a half roll, push through a three quarter loop into a horizontal line, perform a half roll, pull through a three quarter loop into a vertical upline, perform a half roll, push through a quarter loop, exit upright.
半滚
半滚
半滚
P-25.11 半四叶草带半滚
Half Cloverleaf with half roll, half roll, half roll

## Slide 26
P-25.11.02
P-25.11 半四叶草带半滚
Half Cloverleaf with half roll, half roll, half roll
所有圆角半径相等All radii are equal.
半滚位于直线段的中间
½ rolls on middle of the line.

## Slide 27
P-25.12.01
正飞进入，推1/8圆弧进入45°下降直线，做半滚，拉5/8圆弧进入垂直上升直线，连续做两个1/4位滚，拉1/4圆弧，倒飞改出。
From upright, push through a one eighth loop into a forty-five degree downline, perform a half roll, pull through five eighths loop into a vertical upline, perform consecutively two quarter rolls, pull through a quarter loop, exit inverted.
P-25.12 水滴带半滚+1/4位滚
Reverse Figure ET with half roll, two quarter rolls
¼位滚
¼位滚
半滚

## Slide 28
P-25.12.02
¼
¼
两个¼位滚在直线段的中间
¼ rolls centered on middle of the line.
P-25.12 水滴带半滚+1/4位滚
Reverse Figure ET with half roll, two quarter rolls
所有圆角半径相等
All radii are equal.
半滚位于直线段的中间
½ rolls on middle of the line.
¼位滚之间的线段必须短且长度易于辨识。
Lines between part rolls must be short and of recognisable length.

## Slide 29
P-25.13 倒飞螺旋两周带半滚
Inverted Spin two turns, half roll
P-25.13.02
倒飞进入，连续螺旋两周进入垂直下降直线，做半滚，拉1/4圆弧，正飞改出。
From inverted, perform an inverted spin with two turns, perform a vertical downline, perform a half roll, pull through a quarter loop, exit upright.
半滚

## Slide 30
P-25.13.01
强行进入：大幅扣分 Forced entry: downgrade.
螺旋俯冲=0分 Spiral dive - 0 points!
快滚进入=0分 Snap entry - 0 points!
螺旋后保持一段直线
Line after the spins.
P-25.13 倒飞螺旋两周带半滚
Inverted Spin two turns, half roll

## Slide 31
P-25.14.01
P-25.14 礼帽带1/4位滚
Top hat with two quarter rolls. Option: Top hat with quarter roll, quarter roll.
¼ 位滚
¼ 位滚
正飞进入，拉1/4圆弧进入垂直上升直线，连续做两个1/4位滚，拉1/4圆弧进入倒飞直线，拉1/4圆弧进入垂直下降直线，
拉1/4圆弧，正飞改出。
From upright, pull through a quarter loop into a vertical upline, perform consecutively two quarter rolls, pull through a quarter loop into a horizontal line, pull through a quarter loop into a vertical downline, pull through a quarter loop, exit upright.

## Slide 32
P-25.14.02
¼
¼
P-25.14 礼帽带1/4位滚
Top hat with two quarter rolls. Option: Top hat with quarter roll, quarter roll.
所有圆角半径相等
All radii are equal.
两个¼位滚在直线段的中间
¼ rolls centered on middle of the line.
¼位滚之间的线段必须短且长度易于辨识。
Lines between part rolls must be short and of recognisable length.

## Slide 33
P-25.14.03
可选做：正飞进入，拉1/4圆弧进入垂直上升直线，
做1/4位滚，拉1/4圆弧进入倒飞直线，拉1/4圆弧进入垂直下降直线，做1/4位滚，拉1/4圆弧，正飞改出。
Option: From upright, pull through a quarter loop into a vertical upline, perform a quarter roll, pull through a quarter loop into a horizontal line, pull through a quarter loop into a vertical downline, perform a quarter roll, pull through a quarter loop, exit upright.
可选做 Option
¼ roll
¼ roll
P-25.14 礼帽带1/4位滚
Top hat with two quarter rolls. Option: Top hat with quarter roll, quarter roll.

## Slide 34
P-25.14.04
¼位滚位于直线段的中间
¼ rolls on middle of the line.
¼
¼
P-25.14 礼帽带1/4位滚
Top hat with two quarter rolls. Option: Top hat with quarter roll, quarter roll.
可选做 Option
所有圆角半径相等
All radii are equal.

## Slide 35
P-25.15 Z字带快滚
Figure Z with snap roll
P-25.15.01
正飞进入，拉3/8圆弧进入45°上升直线，做一个快滚，推3/8圆弧，正飞改出。
From upright, pull through a three eighths loop into a forty-five degree upline, perform a snap roll, push through a three eighths loop, exit upright.
snap roll
( )

## Slide 36
P-25.15.02
( )
快滚可以是正快滚，也可以是负快滚
Snap roll may be positive or negative.
如果快滚=桶滚或者副翼滚，大幅扣分（＞5分）
If snap roll = barrel roll or aileron roll: Severe downgrade > 5 pts.
45°
快滚在直线段中间
Snap roll on middle of the line.
P-25.15 Z字带快滚
Figure Z with snap roll
所有圆角半径相等
All radii are equal.

## Slide 37
P-25.16.01
P-25.16 彗星带连续1/4位滚+一周滚
Comet with two quarter rolls, roll
¼位滚
¼位滚
一周滚
正飞进入，推1/8圆弧进入45°下降直线，连续做两个1/4位滚，推3/4圆弧进入45°下降直线，做一周滚，拉1/8圆弧，正飞改出。
From upright, push through a one eighth loop into a forty five degree downline, perform consecutively two ¼ rolls, push through a three quarter loop into a forty-five degree downline, perform a roll, pull through a one eighth loop, exit upright.

## Slide 38
P-25.16.02
¼
¼
滚转必须在直线段的中间，
但是不要求在整个动作的中间。
Rolls on middle of the lines, but not necessarily in the center of the manoeuvre.
所有圆角半径相等
All radii are equal.
P-25.16 彗星带连续1/4位滚+一周滚
Comet with two quarter rolls, roll
¼位滚之间的线段必须短且长度易于辨识。
Lines between part rolls must be short and of recognisable length.
滚转位于直线段的中间
Rolls centered on middle of the line.

## Slide 39
P-25.17 S带1/4同步滚
Figure S with quarter roll, quarter roll
P-25.17.01
¼ 同步滚
正飞进入，拉一个半筋斗，在半筋斗靠近顶部的45°圆弧上做1/4同步滚，紧接着向高航线再做一个侧飞半筋斗，在半筋斗靠近顶部的45°圆弧上做1/4同步滚，倒飞改出。
From upright, pull through a half loop while integrating a quarter roll over the top forty-five degrees, perform a half knife-edge loop ending on top level, while integrating a quarter roll over the top forty-five degrees, exit inverted.
¼ 同步滚
45°
45°
侧飞半筋斗
半筋斗

## Slide 40
P-25.17.02
¼同步滚
45°
45°
半筋斗轨迹必须是圆形
Part loops must be round.
¼滚必须在半筋斗靠近顶部的45°圆弧上同步完成。
The ¼ rolls must be integrated on circular flightpath of the 45° segments of the part loops.
两个半筋斗的半径相等
Radii of the part loops are equal.
¼同步滚
P-25.17 S带1/4同步滚
Figure S with quarter roll, quarter roll

## Slide 41
1200
安全线
Safety line
风向
着陆程序
（不计分，不评分）
Landing procedure
( not judged, not scored )
着陆方向可以与起飞方向不同。
The direction of the landing may be different to the take off.

## Slide 42
谢谢观看！
忘记谁在飞
（朋友，竞争对手，同胞，来自其他国家的选手）
忘记什么在飞
（2冲程，4冲程，电动）
只看飞机在天空中描绘的轨迹！
Forget WHO is flying (friend, rival, countryman, flier from other nation)
Forget WHAT is flying (2-stroke, 4-stroke, electric)
LOOK ONLY AT LINES DESCRIBED IN THE SKY!
© Peter Uhlig, February 2023
翻译：Hui Yang F3A 校对：刘爱强 2023年10月
Bob Skinner